## Slide 1: Modelling a submerged Vehicle using ROS (Initial planning for System Design)
Alvydas Juodikis

## Slide 2
Direction of Motion
Pivot point chosen here to represent the upward force that would be present due to buoyancy that opposes the weight of the submerged object
mg
Mg
Assumptions:
Object is stationary and balanced in horizontal position.
No change in yaw or roll, so those components aren’t considered.
g = 9.81ms^-2
Coefficient of resistance = 1
Weight of objects are uniformly distributed. So centre of mass lies in the middle (d/2 m)
Object slides right to the end of hollow vehicle.
m= mass of hollow vehicle (kg)
M = mass of sliding object (kg)
R = Buoyancy
Buoyancy balances out the mass of the submerged vehicle; therefore the sliding mass creates a force at the verse of tipping the vehicle over; however it is still balanced.
mg
Mg
Ѳ
d (m)
1) Model System as simple 2d object (no Yaw or Roll)
2) Establish Pitch angle
B
3) Model Forces
4) Consider turning force for pitch angle
(m)
(m)
B
pitch
Ѳ
Pitch angle corresponding to sliding object mass
Max Distance travelled
Buoyancy
Using Pythagoras Theorem:
Ѳ = arcCos[Mg/()]
Rearranged:
d = Final
d = total length of submerged vehicle
m = mass of the submerged vehicle (kg) M = mass of the sliding vehicle (kg)
B = Buoyancy Ѳ = Pitch angle
Mg
Ѳ
If mass of vehicle (mg) balances buoyancy (B):

## Slide 3: Additional Variables and Assumptions (Solutions to model with greater accuracy)
Coefficient of resistance not taken into account; value given for model = 1 to assume smooth surface. A path with less resistance could be achieved by mounting small wheels or assigning the moving mass to a confined cable set up.
Weight of vehicle assumed to be uniformly distributed; this is likely to be not the case. Upon modelling the exact value of the vehicle, a more realistic position for the centre of mass would be located, along with additional forces that may tip the vehicle.
No change in Yaw or Roll. This could be realistically achieved with Gyroscope and motors for stability. Small minor change in acceleration in those directions activates mini turbines which stabilise vehicle.
Potential collisions with marine life, plants and rubbish in oceans. Image recognition software and ultrasonic sensors. To recognise these object and detect the distance between these objects.
No consideration to the compression or expansion of air in the vehicle. Could be solved with the use of air cylinders that regulate air flow in response to actuators. If compressed air is being measured using a “The MAF (mass air flow) sensor”
Assumptions:
Object is stationary and balanced in horizontal position.
No change in yaw or roll
g = 9.81ms^-2
Coefficient of resistance = 1; assuming smooth surface.
Weight of objects are uniformly distributed. So centre of mass lies in the middle (d/2 m)
Object slides right to the end of hollow vehicle.
m= mass of hollow vehicle (kg)
M = mass of sliding object (kg)
R = Buoyancy
Buoyancy balances out the mass of the submerged vehicle; therefore the sliding mass creates a force at the verse of tipping the vehicle over; however it is still balanced.

## Slide 4: Architecture
Arm cortex m4 with wireless connection to raspberry pie 4, Linux interface (possibly Ubuntu).
Calculations for pitch angle can be done on Cortex M4.
Data from seismometer can be processed on cortex m4 and placed in an array before transfer to raspberry pie 4, for logging data and interpretation.
M4 programs gyroscope to maintain stability.
M4 also deals with ultrasonic sensor, mounted in submerged vehicle, to monitor the distance the sliding object moves.
M4 Stores array for calculated pitch angles, for the different moving distances.
M4 stores values from seismometer for corresponding pitch angles obtained (this can be interpreted later to find the angle the system works most efficiently for different depths the submerged vehicle travels under).

## Slide 5: Architecture
FEEDBACK
SIGNAL
INPUT
Database
Environment
Environmental Data Sent to be processed
(Image and returning Photons)
Ros System
LIDAR
ERROR
SIGNAL
Navigation and Path Planning
Module
Navigation
Stabilisation module for gyroscope
Custom Module
Potential module(s) that deals with the navigation of the submerged vehicle.
Possibly Acoustic USBL positioning system.
Standard ROS navigation using 2D navigation stack that takes in information from sensor streams, goal position and odometry. Will be used for establishing Ocean depth that the vehicle has reached.
Custom
Seisometer
Ultrasonic
USBL
Transiever
Store array for pitch angles for different moving distances.
Store values from seismometer for corresponding pitch angles obtained (this can be interpreted later to find the angle the system works most efficiently for different depth the submerged vehicle travels under).
Calculations for pitch angle can be done on Cortex M4.
Data from seismometer can be processed on cortex m4 and placed in an array before transfer to raspberry pie 4.
Cortex M4
Raspberry Pie 4
Gyroscope to inhibit titling in directions x and z.
Ultrasonic sensor to detect the distance the moving object moves to (this would be mounted at the inner wall of the submerged vehicle).
Negative loop feedback control system to outline erroneous values and be aware of accuracy on reading data

## Slide 6: Pseudo Code for Arm architecture:
Procedure Value_Iteration(M, , g, d)
Inputs
store values as floats: M = mass of sliding object, = Pitch, g = 9.81ms^-2
Outputs
Value for d (distance)
For n iterations (number of values you want to store)
Algorithm
float a = 2*M*g;
Store Value
float b = cos();
Store Value
float d = a/b;
Store Value into Array
sleep(100); delay for 100ms
End
Return;
d =
The Cortex M4 will assign float values to sensor readings, then perform the necessary calculations. This will then be sent to the Rasberry Pi for processing and storing.
Rasberry Pi will also have a series of workspaces and custom modules that deal with stabilisation of the submerged vehicle. As well as the regulation of how far to let the sliding object move forward.

## Slide 7: Regulating Pitch using Raspberry Pi
Raspberry Pi will also have a series of workspaces and custom modules that deal with stabilisation of the submerged vehicle. As well as the regulation of how far to let the sliding object move forward (using a servo motor control).
Centre
Servo Motors
Moving mass
For(pitch< max value)
{
If depth > a
Activate Motor1;
Delay for 100ms;
If depth > b
Activate Motor2;
Delay for 100ms;
If depth > c
Activate Motor3;
Delay for 100ms;
If depth > d
Activate Motor4;
Delay for 100ms;
}
The idea was to have the pitch angle possibly be large when the submerged vehicle has just entered the water, and to then be smaller when entering greater depths. Depths will be measured using Lidar sensors along with the navigation ROS package.
Implementing regulation for the pitch angle by first checking if the pitch angle is less that 90degrees (a set max value);
Then to implement motors to stop the mass from continuously moving too far.
Ultrasonic
Sensor

## Slide 8
Gyroscope to inhibit titling in directions x and z.
Ultrasonic sensor to detect the distance the moving object moves to (this would be mounted at the inner wall of the submerged vehicle).
Lidar sensor used for ocean depth monitoring, through the use of odometry (from the Navigation ROS package).
Seismometer for acquisition of seismic data.
USBL transceiver and transponder for Acoustic USBL positioning communication.
Sensors